/*
Wiring:
  ---------------------
  | VS1053 | ESP32 |
  ---------------------
  | SCK | IO18 |
  | MISO | IO19 |
  | MOSI | IO23 |
  | XRST | EN |
  | CS | IO5 |
  | DCS | IO0 |
  | DREQ | IO4 |
  | 5V | 5V |
  | GND | GND |
  ---------------------

  ---------------------------
  | JMDO 96C-1 OLED | ESP32 |
  ---------------------------
  | SDA | 21 |
  | SCL | 22 |
  | GND | GND |
  | 5V | 5V |
  ---------------------------

  ------------------------------------
  | TFT 2.8 ST7789 | Wroom/Wrover-b |
  ------------------------------------
  | SDA | 21 |
  | SCL | 22 |
  | RST | 15 |
  | DC | 27 |
  | CS | 16/2 |
  | BL | 14 |
  | GND | GND |
  | VCC | 3.3V |
  ---------------------------

  ---------------------------
  | IR module elegoo | ESP32 |
  ---------------------------
  | G | GND |
  | R | 5V |
  | Y | G26/13| wroom/wrover - B ttgo
  ----------------------------

  -----------------------------
  | Pulsanti | ESP32 |
  -----------------------------
  | Vol UP | G32 |
  | Vol Down | G33 |
  | Next Station | G13/34 | wroom/wrover - B ttgo
  | Prv Station | G12 |
  | Radio-Clock Sel | G36/35 | wroom/wrover - B ttgo
  ----------------------------

  ------------------------------
  | Rele comando amplificatore |
  ------------------------------
  | G14/26 |
  ------------------------------

  Il file NexHardware.cpp va modificato per l'uso con seriale 2 del WROVER

  // Modifica per usare la seriale 2 su wrover-b TTGO
    #define RXD2 25
 #define TXD2 26
*/

const int previousButton	= 12;
#ifdef CUCINA
  const int nextButton = 13; // radio cucina
#else
  const int nextButton = 34;
#endif

const int volumeUp	= 32;
const int volumeDown	= 33;
#ifdef WROVER
  const int RCSelector	= 35; // Selettore modalità radio o clock Wrover
  #ifdef HWRCampli
    const int HWRC = 26; // Output comando relè spegnimento ampli audio
  #endif
#endif
#ifdef WROOM
  const int RCSelector	= 36; // Selettore modalità radio o clock Wroom
  #ifdef HWRCampli
    const int HWRC = 17; // Output comando relè spegnimento ampli audio
  #endif
#endif
//IR sensor
//Infrarosso collegato a Pin Esp32
#ifdef WROVER
  const unsigned int kRecvPin	= 13; //26;
#endif
#ifdef WROOM
  const unsigned int kRecvPin	= 26;
#endif
// Pin decodificatore mp3 VS1053
#ifdef ARDUINO_ARCH_ESP32
#define VS1053_CS 5
#define VS1053_DCS 0
#define VS1053_DREQ 4
#define SPI_CLK_PIN 18
#define SPI_MISO_PIN 19
#define SPI_MOSI_PIN 23
#endif

// Pin ST7789
#ifdef ST7789
  #define TFT_SDA 21
  #define TFT_SCL 22
  #define TFT_RST 15
  #define TFT_DC 27
  #ifdef WROVER
    #define TFT_CS 2
  #endif
  #ifdef WROOM
    #define TFT_CS 16
  #endif
  #define TFT_BL 14
#endif
/*
 ---------------------------
  | TFT 2.8 ST7789 | ESP32 | wroom / wrover
  ---------------------------
  | SDA | 21 |
  | SCL | 22 |
  | RST | 15 |
  | DC | 27 |
  | CS | 16/2 |
  | BL | 14 | back light pin
  | GND | GND |
  | VCC | 3.3V |
  ---------------------------
*/

// Modulo radio FM
#ifdef FMMOD // Verificare con Wrover B se questi pin sono ok
  #define PIN_FMWEB 13
  #define PIN_SDAFM 03
  #define PIN_SLCFM 01
#endif